## Overview

Open3S250E is an FPGA development board that consists of the mother board DVK601 and the FPGA core board Core3S250E.

Open3S250E supports further expansion with various optional accessory boards for specific application. The modular and open design makes it the ideal for starting application development with XILINX Spartan-3E series FPGA devices.

## What's on the mother board?

- FPGA CPLD core board connector: for easily connecting core boards which integrate an FPGA CPLD chip onboard, such as Core3S250E

- 8I/Os_1 interface, for connecting accessory boards/modules

- 8I/Os_2 interface, for connecting accessory boards/modules

- 8I/Os_3 interface, for connecting accessory boards/modules

- 8I/Os_4 interface, for connecting accessory boards/modules

- 16I/Os_1 interface, for connecting accessory boards/modules

- 16I/Os_2 interface, for connecting accessory boards/modules

- 32I/Os_1 interface, for connecting accessory boards/modules

- 32I/Os_2 interface, for connecting accessory boards/modules

All the I/O interfaces above:

- Capable of being simulated as USART, I2C, SPI, PS/2, etc.

- Capable of driving devices such as FRAM, FLASH, USB, Ethernet, etc.

- FPGA expansion connectors

  - FPGA pins are accessible on expansion connectors

  - for connecting SDRAM accessory board

- LCD interface, for connecting LCD22, LCD12864, LCD1602

- ONE-WIRE interface: easily connects to ONE-WIRE devices (TO-92 package), such as temperature sensor (DS18B20), electronic registration number (DS2401), etc.

- Buzzer

- Joystick: five positions

- Potentiometer: for LCD22 backlight adjustment, or LCD12864, LCD1602 contrast adjustment

- Buzzer jumper

- Joystick jumper

- ONE-WIRE jumper

For jumpers 16-18:

- short the jumper to connect to I/Os used in example code

- open the jumper to connect to other custom pins via jumper wires

## What's on the Core3S250E?

- XC3S250E: the XILINX Spartan-3E FPGA device which features:

  - Operating Frequency: 50MHz

  - Operating Voltage: 1.15V～3.3V

  - Package: QFP144

  - I/Os: 80

  - LEs: 250K

  - RAM: 216kb

  - DCMs: 4

  - Debugging/Programming: supports JTAG

- AMS1117-3.3 (on bottom side), 3.3V voltage regulator

- AMS1117-2.5 (on bottom side), 2.5V voltage regulator

- AMS1117-1.2 (on bottom side), 1.2V voltage regulator

- XCF02S (on bottom side), onboard serial FLASH memory, for storing code

- Power indicator

- LEDs

- FPGA initialization indicator

- Reset button

- nCONFIG button: for re-configuring the FPGA chip, the equivalent of power resetting

- Power switch

- 50M active crystal (on bottom side)

- 5V DC jack

- JTAG interface: for debugging/programming

- FPGA pins expander, VCC, GND and all the I/O ports are accessible on expansion connectors for further expansion

- LED jumpers

## Photos

Open3S250E Development Board

Mother Board DVK601

FPGA core board Core3S250E

FPGA core board Core3S250E

Connecting to various peripherals

Connecting to LCD12864

Connecting to LCD1602

Connecting to RS232 Board

Connecting to USB UART Board

Connecting to 8 SEG LED Board

Connecting to 8 Push Buttons

Connecting to 4x4 Keypad

Connecting to EEPROM Board

Multi peripherals connected to one interface

Connecting to Data Flash Board

Connecting to CY7C68013A USB Board

Connecting to VGA PS2 Board

Connecting to any accessory board you need

Note: The Open3S250E does NOT integrate any programming/debugging function; a programmer/debugger is required.

## Examples

The Open3S250E FPGA development board comes with various examples codes for the supported peripherals, which give you a quick start to develop your own application.

| Peripheral | Description | Interface | Verilog | VHDL |
| --- | --- | --- | --- | --- |
| AT24CXX | EEPROM | I2C | Y | Y |
| FM24CXX | FRAM | I2C | Y | Y |
| AT45DBXX | DATAFLASH | SPI | Y |  |
| PCF8563 | RTC | I2C | Y |  |
| PCF8591 | 4xAD, 1xDA | I2C | Y |  |
| DS18B20 | Temperature sensor | 1-WIRE | Y |  |
| SP3232 | Serial communication | UART | Y | Y |
| SP3485 | Serial communication | UART | Y | Y |
| PL2303 | USB TO UART | UART | Y | Y |
| CY7C68013A | USB DEVICE | I/Os |  | Y |
| Buzzer | Sound device | 1I/O (PWM) | Y | Y |
| PS/2 keyboard | Input device | PS/2 | Y | Y |
| Single buttons | Input device | ---- | Y | Y |
| 4x4 keypad | Input device | 8I/Os | Y | Y |
| Joystick | Input device | 5I/Os | Y | Y |
| LED | Display device | ---- | Y | Y |
| 8 SEG LED | Display device | 13I/Os | Y | Y |
| VGA monitor | Display device | VGA | Y | Y |
| Character LCD | Display device | 11I/Os | Y | Y |
| Graphic LCD | Display device | 11I/Os | Y | Y |

## Debugging/Programming Interface

The Open3S250E FPGA development board integrates JTAG interface for programming/debugging.

### JTAG Signal Names & Description

| Pin | Signal Name | Description |
| --- | --- | --- |
| 1 | GND | Signal ground |
| 2 | VCC(TRGT) | Target power supply |
| 3 | GND | Signal ground |
| 4 | TMS | JTAG state machine control |
| 5 | GND | Signal ground |
| 6 | TCK | Clock signal |
| 7 | GND | Signal ground |
| 8 | TDO | Data from device |
| 9 | GND | Signal ground |
| 10 | TDI | Data to device |
| 11 | GND | Signal ground |
| 12 | NC |  |
| 13 | GND | Signal ground |
| 14 | NC |  |
| 15 | GND | Signal ground |

### JTAG Header Pin out

## Development Resources

The Open3S250E FPGA development board comes with a User Guide CD including development resources listed as below:

- Related software (Xilinx ISE 12)

- Demo code (Verilog, VHDL)

- Schematic (PDF)

- FPGA development documentations